## Slide 1
MagSail CubeSat Flight Experiment
Revision 05 (1U CubeSats)
Jan 21, 2021
(Revised mass budget, smaller battery)

## Slide 2
High-level requirements
Design a CubeSat flight experiment to test the hypothesis that magsails can serve as a viable deorbit method for satellites in Low Earth orbits (700-1400 km).
Design drivers:
  low-cost
  flexible and frequent launch options,
  ability to conclusively detect the magsail drag effects
  simple deployment mechanism,
  possibly demonstrate deorbit (re-entry) in 100 days
  use proven COTS parts with flight-heritage

## Slide 3
Baseline mission concept
The reference design consists of 2 “1U” cubesats to start with, with minimal capability
  to see what can be done with 1U (“minimal” experiment)
Cubesat #1 has magsail energized with 1.4 W.
  4 deployable booms 50 cm each creates current “square”
  Magsail On during sunlight, off during eclipse
  Other cubesat will not have magsail turned on.
Both satellites should drift by several thousand kilometeres in about 3 weeks (to be checked at the end).

## Slide 4
Key trades (1 of 2)
Orbit altitude: 420 km, 750 km, GTO
  selected primarily due to ease of access and magsail effectiveness
Form factor: 1U, 1.5U, 2U, 3U
  to see what can be done with 1U
Number of satellites: 1, 2
  two identical satellites with one magsail energized will be able to conlusively detect the effect of magsail drag and cancel out aerodynamic drag, solar radiation pressure etc.
Attitude control: none, passive (permanent magnet, gravity gradient, spin about max MoI axis), active (mag.torquer, reaction wheels)
  no driving attitude requirements, passive for low cost
  lightweight permanent magnets can align one axis with the Earth’s field, and improve downlink, more reliable GPS lock.

## Slide 5
Key trades (2 of 2)
Solar panels: fixed, deployable, articulated
  low cost, reliable
Batteries: Li-ion, Li-Po,Ni-Cd, supercapacitors
  low-cost, high Wh/kg, low vol/kg, high-discharge current, commercial, flight-heritage
Telecom: UHF (ground station), L-band (Iridium).
  low cost, less regulatory hurdles, no poiniting required
Antenna: deployable monopole, patch.
  flight-heritage
Processor and data handling:
  commericial off the shelf, need not be rad hard, redundancy with cross-strap architecture

## Slide 6
Power (1 of 3) - power budget (revised)
TX on only 0.5 sec per minute, 0.2 W

## Slide 7
Power (2 of 3) - Battery (revised)
1 X LG LGIP-520B Li Ion
= 3.7 Wh, 23g, $9
see next slide for battery discharge during operation
Lower Wh battery than before, 23 g instead of 100g
Recommend 2 in parallel for redundancy, and higher battery capacity

## Slide 8
Power (3 of 3) - Battery charge
Magsail ON during sunlight, P = 1.5W
Magsail turned off for 4 hours every 48 hours to replenish battery

## Slide 9
Telecom (1 of 3)
Reference: VHF/UHF, ground station
            Nominal TX power: 0.2 W
            Duty cycle: 0.5 second beep every minute
            Desired data rate: ~ 10 kbps, total data = 5 kb per beep
            Link budget in next page
            Link has to be closed (margin > few dB)

## Slide 10
Telecom (2 of 3) - Link budget

## Slide 11
Attitude control (1 of 2)
No attitude control for reference 1U.
Attitude control system not necessary, however more analysis is required. Need to detumble before deployment?
It may help to have a few permanent magnets (< 50 g) along the magsail axis so it stabilizes the magsail axis along the ambient field. (or use magnetotorquers)

## Slide 12
Attitude control (2 of 2)
May help data download and GPS reception.
Some addtional analysis is being done.

## Slide 13
Tracking (1 of 2)
A low mass, low power GPS receiver is added
  Mass = 9 g, power = 0.15 W, time to first fix ~ 90s

## Slide 14
Tracking (2 of 2)
Other options:
  NORAD tracking data
Commercial radar observations (LeoLabs)

## Slide 15
Mass budget (Jan 21)

## Slide 16
Raspberry Pi as On Board computer?
$20 computer
9g, 0.4W
Can use 2 boards for redundancy

## Slide 17
Drawing (Work in progress)

## Slide 18
Deployment demo (in progress).

## Slide 19
Deployment demo (in progress).

## Slide 20
Deployment demo (in progress).

## Slide 21
Deployment demo (in progress).
Deployment with rolled up tape spring is unstable, this problem is solved by composite tape springs which deploy much more predictably. However, these are not readily available for purchase. But if we move to a flight experiment, we should be able to get them.
However, we may be able to show some kind of demonstration with ordinary tape spring.
Will try again tomorrow.

## Slide 22
Orbit decay

## Slide 23
Relative separation